# GAY-LUSSAC’S LAW

Pressure and Temperature are directly proportional.

P	=  k    			P1      P2

## T      			 	T1      T2

Boyle’s		Charles’		Gay-Lussac’s

PV		    V				P

T				T

# PV			COMBINED GAS LAW

T

Ex: A gas sample at 28(C and 1.26 atm has a volume of 13.8L.

What would the volume be if the pressure was 7.40 atm and

the temperature was 34(C?

P1V1	     P2V2	      1.26atm(13.8L)      7.40atm(V2)

T1	       T2		      301K		           307K

V2 = 1.26(13.8)307	      2.40 L

301(7.40)

STP = standard temperature and pressure

0(C, 273K           1 atm